## Slide 1: Eulerian Video Magnifacation
Feb 22, 2016
Luis Alberto Díaz de León

## Slide 2
Notes: This represents how the algorithm works

## Slide 3: reproduceresults.m
amplify_spatial_lpyr_temporal_iir
(vidFile,
resultsDir,
alpha,
lambda_c,
r1,
r2,
chromAttenuation)
amplify_spatial_lpyr_temporal_butter
(vidFile,
outDir,
alpha,
lambda_c,
fl,
fh,
samplingRate,
chromAttenuation)
Notes: Challenge: Remove Sampling Rate from the input, it can be calculated later

## Slide 4: amplify_spatial_lpyr_temporal_iir.m
Spatial Filtering: Laplacian pyramid
Temporal Filt: substraction of two IIR lowpass filters
y1[n] = r1*x[n] + (1-r1)*y1[n-1]
y2[n] = r2*x[n] + (1-r2)*y2[n-1]
(r1 > r2)
y[n] = y1[n] - y2[n]
Notes: Function deffinition

## Slide 5: amplify_spatial_lpyr_temporal_iir.m
vid = VideoReader(vidFile); %Read Video
vidHeight = vid.Height;
vidWidth = vid.Width;
fr = vid.FrameRate;
len = vid.NumberOfFrames;
startIndex = 1;
endIndex = len-10;
Notes: Challenge: do not remove ten frames from endIndex, this makes the output video smaller causing confusion and difficult to compare with original.

## Slide 6: amplify_spatial_lpyr_temporal_iir.m
frame= struct('cdata', zeros(vidHeight, vidWidth, nChannels, 'uint8'), 'colormap', []);
frame.cdata = read(vid, startIndex);
.
.
[pyr,pind] = buildLpyr(frame(:,:,1),'auto');
pyr = repmat(pyr,[1 3]);
[pyr(:,2),~] = buildLpyr(frame(:,:,2),'auto');
[pyr(:,3),~] = buildLpyr(frame(:,:,3),'auto');
Notes: nChannels =3 (RGB)
Handles first frame at the baggining to make a three-dimentional matrix
Challenge: calculate pyr size prior to the pyramid calculation to make a footprint and save RGB in one single loop

## Slide 7: amplify_spatial_lpyr_temporal_iir.m
lowpass1 = (1-r1)*lowpass1 + r1*pyr;
lowpass2 = (1-r2)*lowpass2 + r2*pyr;
filtered = (lowpass1 - lowpass2);
Notes: Temporal filtering

## Slide 8: amplify_spatial_lpyr_temporal_iir.m
delta = lambda_c/8/(1+alpha);
lambda = (vidHeight^2 + vidWidth^2).^0.5/3;
%inside loop
currAlpha = lambda/delta/8 - 1;
lambda = lambda/2;
Notes: Challenge: /3 Experimental Constant
currAlpha = currAlpha*exaggeration_factor;

## Slide 9: amplify_spatial_lpyr_temporal_iir.m
If (currAlpha > alpha)
% representative lambda exceeds lambda_c
filtered(indices,:) = alpha*filtered(indices,:);
else
filtered(indices,:) = currAlpha*filtered(indices,:);

## Slide 10: amplify_spatial_lpyr_temporal_iir.m
The lambda_c used in the code, is the one shown in the figure below. It is used initialy in the source code to compute Delta.
Other part of code calculates lambda, on each one of the parts of the pyramid.
The Delta calculated with lambda_c and the lambda are then used to calculate the current alpha.
If current alpha exceeds the alpha from the input parameter, that means that lambda is greated than lambda_c, si the alpha in the input parameters is used to amplify. Otherwise means that lambda is smaller than lambda_c, so the alpha calculated is used to attenuate the pyramid part.